## Slide 1: EU POWER MARKET INSIGHT
VS
MARKET ANALYSIS 2022-2050
GB
DE

## Slide 2: Table of Content EU Power Market Insight: GB vs DE Analysis (2022-2050)
1
Executive Summary
📊
2
Baseload Price Analysis
⚡
3
Generation Mix Impact
🔋
4
Capture Price Comparison
💰
5
Correlation Analysis
📈
6
Forecast Changes
🔄

## Slide 3: Looking Back from 2050: Did Our Investments Deliver Value? Two paths, one destination — which investment strategy leads to success?
Chart: 
| Category 1 | Category 2 | Category 3
Series 1 | 4.3 | 2.5 | 3.5
Start
2050
Forecast Data
2022Q3 / 2023Q1
💨
Onshore Wind
Germany
Solar PV
Great Britain
☀️
⚡
💰
The Future
Did we choose wisely?
What This Analysis Shows
How capture and baseload prices diverge across both countries, and what this means for strategic investment decisions.
The Critical Question
Imagine Standing at 2050, looking back Britain and Germany will have invested trillions in renewables, yet the question remains did those investments deliver value at the right time?
Our Outcome
Know which technology wins and what decisions to make today.

## Slide 4: Executive Summary Comparing GB and DE Market Outlooks (2022Q3 vs 2023Q1)
Germany’s Onshore Wind Shows Strong Long-term Price Stability While Britains’s Solar PV Offers Higher Growth But Greater Volatility
📈 2022-2023 Pattern
2022 Q3: DE started +44% higher than GB, then converged
2023 Q1: GB started +124% higher than DE, declined together
Price Generation Mix
Strong negative correlation: more generation = lower prices
-0.70 → -0.82
Wind Q3 Wind Q1
-0.89
Solar (Both)
⚠️ Critical Strategic Insight
Forecasts shifted significantly between Q3 and Q1, with Solar PV gaining 24% and Onshore Wind gaining 8%. The strengthening negative correlation (-0.70 → -0.82) signals increasing market saturation concerns as renewable capacity grows.
Long Term Technology Winner
Solar PV (GB) emerges as the more valuable long-term investment in both forecasts
2022 Q3
Wins post-2029
2022 Q3
Consistently Higher
Median Capture Price
2022 Q3
Solar (GB) €50
Wind (DE) €53
Solar +24% | Wind +8%
2023 Q1
Solar (GB) €62
Wind (DE) €57
💨
☀️
💨
☀️
💰
Median Baseload Price
2022 Q3
GB €67
DE €66
GB +€3 | DE +€15
2023 Q1
GB €70
DE €81
💰

## Slide 5
Chart: 
| "22 | "23 | "24 | "25 | "26 | "27 | "28 | "29 | "30 | "31 | "32 | "33 | "34 | "35 | "36 | "37 | "38 | "39 | "40 | "41 | "42 | "43 | "44 | "45 | "46 | "47 | "48 | "49 | "50
GB | 197.2282 | 170.1329 | 131.653 | 106.4434 | 89.7797 | 85.4604 | 80.6315 | 74.9458 | 72.1666 | 73.3246 | 72.595 | 73.9962 | 74.1467 | 72.0623 | 73.2088 | 73.3014 | 72.236 | 72.4908 | 71.4139 | 69.9432 | 68.7852 | 67.2798 | 66.2029 | 66.5734 | 66.3534 | 67.1872 | 66.1218 | 67.4767 | 66.6545
DE | 283.4848 | 305.18 | 206.7084 | 150.2342 | 119.3249 | 109.7229 | 94.2997 | 78.965 | 69.1868 | 67.2693 | 64.234 | 63.0558 | 63.2599 | 62.2205 | 61.4627 | 61.8531 | 61.0272 | 62.1701 | 60.0197 | 60.5533 | 60.0725 | 59.4054 | 58.2996 | 56.2409 | 57.5586 | 56.817 | 55.1493 | 54.9748 | 53.8053
2022 Q3
Baseload Price Trend
2022 Q3
Price Evolution
Baseload Price Comparison: GB VS DE How do wholesale power prices (baseload) compare between GB and DE?
💡Wholesale baseload prices show significant initial divergence between GB and DE, but converge to similar levels over time as both markets mature.
2022
2023
2050
GB €283
DE €197
DE started 44% higher
GB €283
DE €197
DE picked while GB declined
GB €283
DE €197
Converged, GB slightly higher

## Slide 6: Baseload Price Comparison: GB VS DE How do wholesale power prices (baseload) compare between GB and DE?
2023 Q1
Baseload Price Trend
Chart: 
| "23 | "24 | "25 | "26 | "27 | "28 | "29 | "30 | "31 | "32 | "33 | "34 | "35 | "36 | "37 | "38 | "39 | "40 | "41 | "42 | "43 | "44 | "45 | "46 | "47 | "48 | "49 | "50
GB | 260.064 | 197.2074 | 144.8658 | 98.1984 | 92.9874 | 89.5134 | 83.7234 | 79.902 | 80.3652 | 79.7862 | 80.5968 | 79.7862 | 76.7754 | 76.1964 | 74.9226 | 73.0698 | 73.1856 | 73.1856 | 70.2906 | 68.5536 | 66.585 | 66.585 | 65.7744 | 65.1954 | 64.0374 | 62.6478 | 63.4584 | 64.269
DE | 116.2808 | 118.6233 | 107.8378 | 92.5563 | 86.9841 | 85.8144 | 83.8903 | 80.8085 | 78.1112 | 75.656 | 76.9221 | 75.2765 | 75.7615 | 76.0049 | 76.6461 | 76.5203 | 76.675 | 74.745 | 75.4383 | 74.7484 | 71.3781 | 70.2345 | 69.6152 | 68.1025 | 67.8645 | 66.3925 | 65.9248 | 64.1613
2023 Q1
Price Evolution
💡GB and DE wholesale prices start from opposite positions (GB higher), then rapidly converge and remain closely aligned throughout the forecast period.
2023
2025
2050
GB €260
DE €116
GB Started 124% higher
GB €93
DE €93
Both converged rapidly
GB €70
DE €77
Remained closely aligned

## Slide 7
2022 Q3
Generation Mix in GB
Baseload Price Comparison: GB VS DE Does their respective power generation mix explain the difference?
✅ Yes. DE's lower initial renewable share (<30%) explains the higher starting prices, while GB's offshore wind dominance and faster renewable growth drove earlier price declines and convergence
Chart: 
| "22 | "23 | "24 | "25 | "26 | "27 | "28 | "29 | "30 | "31 | "32 | "33 | "34 | "35 | "36 | "37 | "38 | "39 | "40 | "41 | "42 | "43 | "44 | "45 | "46 | "47 | "48 | "49 | "50
Fossil & Other Thermal | 12.37 | 14.21 | 11.67 | 9.58 | 9.58 | 9.58 | 9.6 | 9.58 | 9.58 | 9.58 | 9.6 | 9.58 | 9.58 | 9.58 | 9.6 | 9.58 | 12.19 | 12.2 | 12.19 | 12.14 | 14.62 | 14.53 | 14.48 | 14.42 | 14.35 | 14.32 | 14.22 | 14.23 | 14.14
Gas & Hydrogen | 93.27 | 100.54 | 94.5 | 92.75 | 73.18 | 72.11 | 60.5 | 48.97 | 43.99 | 40.93 | 38.62 | 40.53 | 38.14 | 34.32 | 36.78 | 36.98 | 34.91 | 33.78 | 30.17 | 27.12 | 18.59 | 18.8 | 19.39 | 20.45 | 19.74 | 20.08 | 20.04 | 21.69 | 22.7
Interconnectors | 21.42 | 10.46 | 14.26 | 14.95 | 17.63 | 21.34 | 23.37 | 14.89 | 10.96 | 10.39 | 13.95 | 17.16 | 15.86 | 12.52 | 10.9 | 10.91 | 5.3 | 4.47 | 4.77 | 2.02 | 5.47 | 5.81 | 6.43 | 8.11 | 3.79 | 2.96 | 1.1 | 2.28 | 4.69
Nuclear | 44.79 | 37.82 | 30.36 | 22.94 | 22.62 | 15.33 | 14.4 | 27.19 | 33.52 | 33.41 | 33.6 | 33.65 | 40.28 | 53.26 | 59.94 | 64.38 | 73.43 | 78.08 | 83.73 | 94.38 | 99.86 | 99.83 | 100.13 | 105.54 | 116.27 | 121.66 | 121.83 | 121.49 | 121.35
Offshore Wind | 44.78 | 49.6 | 59.16 | 70.92 | 86.18 | 98.91 | 114.26 | 130.41 | 141.33 | 149.98 | 154.24 | 154.82 | 157.37 | 158.29 | 161.06 | 161.95 | 163.68 | 166.44 | 168.91 | 171.15 | 172.78 | 177.16 | 180.15 | 179.38 | 178.47 | 180.72 | 188.36 | 191.18 | 193.81
Onshore Wind | 31.88 | 34.37 | 37.75 | 42.6 | 48.51 | 52.7 | 57.72 | 58.24 | 58.03 | 57.97 | 59.27 | 59.36 | 58.81 | 58.96 | 59.45 | 59.7 | 60.59 | 60.75 | 61.3 | 60.27 | 60.12 | 61.71 | 64.61 | 64.56 | 64.03 | 63.24 | 63.52 | 62.92 | 62.99
Other | 53 | 55.93 | 56.07 | 53 | 50.85 | 42.73 | 36.66 | 33.86 | 32.18 | 31.75 | 31.76 | 32.15 | 32.01 | 31.07 | 25.63 | 26.16 | 25.92 | 25.91 | 25.84 | 25.66 | 26.39 | 26.46 | 26.4 | 26.45 | 26.35 | 26.51 | 26.38 | 26.54 | 26.45
Solar Pv | 12.46 | 12.76 | 13.61 | 14.85 | 17.21 | 19.25 | 21.32 | 22.31 | 46.72 | 48.62 | 25.57 | 26.8 | 28.06 | 29.29 | 30.95 | 32.07 | 33.49 | 35.56 | 37.74 | 39.77 | 41.82 | 44.51 | 46.8 | 48.68 | 51.9 | 53.22 | 55.31 | 56.74 | 58.26
2022 Q3
Generation Mix in DE
Chart: 
| "22 | "23 | "24 | "25 | "26 | "27 | "28 | "29 | "30 | "31 | "32 | "33 | "34 | "35 | "36 | "37 | "38 | "39 | "40 | "41 | "42 | "43 | "44 | "45 | "46 | "47 | "48 | "49 | "50
Biomass And Waste | 71.0376 | 75.7797 | 79.632 | 83.5995 | 88.1737 | 92.9327 | 96.9631 | 100.0266 | 100.9968 | 100.6775 | 100.2443 | 97.6368 | 96.222 | 95.0419 | 94.1803 | 93.9064 | 94.2003 | 94.345 | 92.5548 | 92.5514 | 91.6523 | 91.2816 | 91.7552 | 90.3725 | 90.8709 | 90.4062 | 88.6247 | 87.7962 | 87.3485
Biomass Ccs | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Fossil & Other Thermal | 201.966 | 200.5178 | 175.1275 | 155.0308 | 105.9914 | 97.5169 | 73.0782 | 53.5115 | 43.0244 | 31.7987 | 29.6901 | 28.2997 | 23.9052 | 16.3844 | 15.9385 | 15.0367 | 9.9918 | 1.2442 | 0.91011 | 0.96923 | 0.96329 | 0.64417 | 0.63482 | 0.6135 | 0.31883 | 0.34042 | 0.3286 | 0.0062234 | 0.003224
Gas & Hydrogen | 76.1599 | 77.5932 | 91.7992 | 112.5941 | 127.3296 | 126.1442 | 131.7774 | 132.2823 | 128.957 | 128.7657 | 123.8572 | 124.9595 | 126.4265 | 127.1607 | 129.2912 | 130.0777 | 131.0055 | 134.6712 | 130.7025 | 128.3018 | 126.9167 | 124.9083 | 124.3139 | 121.3025 | 120.6047 | 119.5729 | 117.7263 | 116.3827 | 113.6996
Hydro | 15.0973 | 15.1849 | 15.1379 | 15.0948 | 14.9852 | 14.9378 | 14.7339 | 14.4754 | 14.2045 | 14.0069 | 13.9194 | 13.8364 | 13.8824 | 14.1215 | 14.0589 | 14.1335 | 14.0999 | 14.1386 | 14.247 | 14.0585 | 13.8987 | 13.9177 | 13.7522 | 13.7299 | 13.6871 | 13.4663 | 13.463 | 13.2804 | 13.2135
Nuclear | 31.6881 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Offshore Wind | 28.5511 | 29.7651 | 31.7558 | 36.5796 | 41.9912 | 45.8388 | 50.7833 | 62.3339 | 84.8273 | 93.7523 | 103.3517 | 111.8714 | 121.0152 | 130.5483 | 131.1654 | 137.9775 | 145.3327 | 152.6034 | 161.115 | 166.7964 | 172.2727 | 178.363 | 185.2185 | 190.518 | 195.0957 | 201.0147 | 207.2137 | 212.1752 | 217.3345
Onshore Wind | 97.3612 | 102.5356 | 108.0948 | 114.1355 | 120.338 | 124.1948 | 129.4215 | 134.7115 | 142.4632 | 147.7797 | 154.2243 | 158.3626 | 163.5699 | 169.6609 | 171.3696 | 175.2304 | 179.8777 | 185.1855 | 192.1958 | 200.0633 | 209.0189 | 218.0196 | 227.0235 | 233.8352 | 241.3846 | 248.3547 | 257.4996 | 264.5159 | 270.9636
Solar Pv | 59.0549 | 66.1512 | 74.7561 | 85.5252 | 98.9136 | 113.2669 | 128.0825 | 140.9485 | 153.4303 | 155.1294 | 157.5174 | 159.0235 | 161.2045 | 163.716 | 165.3756 | 167.0274 | 169.0559 | 170.8539 | 172.9257 | 174.4019 | 176.8396 | 179.0283 | 180.8993 | 183.4316 | 185.1743 | 188.5927 | 191.6172 | 193.3678 | 195.6096
▸Offshore wind dominate (20% to 35%)
▸Renewables grew <25% to 50%, displacing fossil
▸Diverse mix with nuclear, gas and others
▸Low starting point (<30% renewables = high prices)
▸Balanced mix of solar, onshore & offshore wind
▸Converges to ~60% renewables alongside GB

## Slide 8
2023 Q1
Generation Mix in GB
Baseload Price Comparison: GB VS DE Does their respective power generation mix explain the difference?
✅ Yes. GB's higher starting prices correlate with similar renewable penetration patterns to DE in this forecast, with both markets showing parallel renewable growth trajectories leading to price alignment.
2023 Q1
Generation Mix in DE
Chart: 
| "41 | "38 | "39 | "36 | "40 | "42 | "37 | "43 | "44 | "46 | "48 | "47 | "45 | "49 | "50 | "35 | "32 | "31 | "34 | "33 | "30 | "29 | "28 | "27 | "26 | "23 | "25 | "24
Fossil & Other Thermal | 12.14 | 12.21 | 12.22 | 9.6 | 12.25 | 14.75 | 9.58 | 14.74 | 14.75 | 14.75 | 14.75 | 14.83 | 14.81 | 14.71 | 14.7 | 9.58 | 9.6 | 9.58 | 9.58 | 9.58 | 9.58 | 9.58 | 9.6 | 9.58 | 9.58 | 12.66 | 9.56 | 10.88
Gas & Hydrogen | 21.9 | 28.27 | 27.27 | 30.7 | 25.09 | 15.95 | 30.43 | 15.88 | 16.3 | 15.48 | 14.91 | 15.08 | 16.95 | 15.9 | 17.65 | 29.63 | 34.66 | 38.23 | 32.85 | 35.72 | 42.32 | 48.36 | 58.38 | 66.87 | 68.09 | 98.1 | 83.69 | 87.69
Interconnectors | -13.53 | -7.22 | -8.7 | -1.62 | -7.85 | -13.62 | -0.7 | -14.41 | -12.23 | -13.12 | -16.46 | -15.68 | -10.24 | -13.02 | -10.6 | -0.27 | -0.01 | -3.79 | 3.96 | 4.55 | -2.61 | 1.72 | 14.86 | 16.93 | 19.32 | 8.65 | 20.91 | 16.28
Nuclear | 94.17 | 73.52 | 78.09 | 60.18 | 83.83 | 99.9 | 64.59 | 99.97 | 100.38 | 116.53 | 122.09 | 121.88 | 105.7 | 121.68 | 121.61 | 53.48 | 33.84 | 33.6 | 40.42 | 33.85 | 33.79 | 27.4 | 14.6 | 15.36 | 22.64 | 37.82 | 22.94 | 30.36
Offshore Wind | 181.48 | 175.26 | 176.81 | 172.08 | 178.81 | 184.34 | 172.9 | 190.68 | 193.69 | 192.19 | 199.53 | 195.35 | 193.45 | 200.65 | 201.3 | 168.02 | 163.09 | 157.08 | 166.2 | 163.6 | 146.42 | 135.28 | 119.86 | 104.94 | 90.11 | 49.66 | 70.71 | 59.22
Onshore Wind | 72.27 | 67.66 | 70 | 65.97 | 68.94 | 71.83 | 66.32 | 73.25 | 73 | 71.71 | 75.51 | 72.8 | 72.15 | 74.86 | 74.88 | 64.81 | 65.22 | 64.48 | 64.42 | 64.78 | 64.55 | 63.57 | 60.08 | 53.79 | 46.44 | 33.19 | 38.89 | 36.99
Other | 25.51 | 25.93 | 26.07 | 26.36 | 26.44 | 26.58 | 26.59 | 26.6 | 27.33 | 27.52 | 27.55 | 27.55 | 27.61 | 28.07 | 28.71 | 32.27 | 33.75 | 33.79 | 33.97 | 34.29 | 34.31 | 36 | 38.43 | 44.46 | 52.25 | 55.63 | 56.57 | 56.61
Solar Pv | 40.65 | 35.51 | 37.15 | 32.32 | 38.8 | 42.5 | 33.92 | 44.89 | 46.86 | 50.8 | 53.52 | 51.79 | 48.18 | 54.56 | 55.68 | 30.56 | 27.05 | 51.9 | 29.35 | 28.16 | 24.73 | 23.27 | 21.83 | 19.41 | 17.1 | 12.4 | 14.69 | 13.68
▸Similar renewable trajectory to 2022 Q3 forecast
▸Offshore wind remains dominant, growing steadily
▸ Converges to ~30% renewables
▸Parallel growth pattern with GB in this scenario
▸Balanced mix of solar, onshore & offshore wind at the end
▸Converges to ~90% renewables 60% more than GB
Chart: 
| "23 | "24 | "25 | "26 | "27 | "28 | "29 | "30 | "31 | "32 | "33 | "34 | "35 | "36 | "37 | "38 | "39 | "40 | "41 | "42 | "43 | "44 | "45 | "46 | "47 | "48 | "49 | "50
Biomass And Waste | 60.5281 | 64.4455 | 63.0425 | 62.5545 | 61.9428 | 61.7666 | 60.9688 | 56.5276 | 56.3174 | 55.9694 | 55.7098 | 55.2467 | 51.4405 | 51.3828 | 51.1765 | 49.9577 | 48.9629 | 45.2382 | 44.9094 | 43.9188 | 42.5607 | 41.9141 | 38.0096 | 36.5672 | 35.9724 | 35.6193 | 33.5602 | 31.8335
Fossil & Other Thermal | 152.3081 | 139.9075 | 109.8587 | 63.6656 | 51.1479 | 42.503 | 39.1765 | 30.3653 | 17.376 | 12.6528 | 12.1557 | 11.8221 | 5.3881 | 4.8649 | 4.7863 | 0.019298 | 0.012238 | 0.00941 | 0.015095 | 0.01031 | 0.002295 | 0.00043 | 0 | 0 | 0 | 0 | 0 | 0
Gas & Hydrogen | 117.0742 | 108.0204 | 126.3249 | 130.6512 | 130.2422 | 127.3454 | 121.5427 | 115.1032 | 111.5368 | 106.113 | 102.6349 | 102.1352 | 95.6795 | 92.6723 | 84.9647 | 81.7924 | 77.1107 | 67.7943 | 65.4484 | 54.1034 | 50.3119 | 44.8722 | 43.3156 | 39.9525 | 38.8692 | 37.581 | 34.5599 | 33.8869
Hydro | 15.1574 | 15.1561 | 15.103 | 14.8889 | 14.667 | 14.4115 | 14.0586 | 13.6973 | 13.6327 | 13.5936 | 13.4778 | 13.5012 | 13.7183 | 13.6906 | 13.6191 | 13.7035 | 13.6616 | 13.8021 | 13.5676 | 13.4277 | 13.2349 | 13.0251 | 12.9811 | 12.8943 | 12.6685 | 12.4808 | 12.4318 | 12.2341
Offshore Wind | 28.9254 | 30.5229 | 35.1045 | 41.7147 | 47.259 | 51.5191 | 62.904 | 85.5269 | 95.0918 | 105.0052 | 113.8334 | 122.8625 | 133.0772 | 148.6982 | 163.7555 | 179.4696 | 194.5874 | 211.8345 | 228.7509 | 246.4207 | 264.3531 | 282.9548 | 300.6691 | 304.0831 | 308.2073 | 312.8411 | 315.8637 | 319.7069
Onshore Wind | 104.7114 | 107.4179 | 114.1662 | 124.4694 | 131.1696 | 138.8635 | 145.5152 | 153.8291 | 165.4316 | 178.5449 | 188.3396 | 199.5713 | 211.9586 | 224.6359 | 235.7711 | 248.4913 | 261.4531 | 276.8337 | 287.9857 | 300.7181 | 313.9685 | 326.8362 | 334.1544 | 343.4827 | 352.3303 | 363.7067 | 372.5638 | 381.8536
Solar Pv | 68.0411 | 75.6087 | 85.9639 | 99.3323 | 113.5182 | 127.8317 | 141.1103 | 154.5534 | 158.7278 | 163.7035 | 167.3149 | 171.7216 | 176.9084 | 183.7582 | 190.2224 | 196.9142 | 202.0905 | 207.7326 | 213.1141 | 218.5609 | 223.6844 | 228.4859 | 233.7152 | 237.7129 | 242.2426 | 247.5861 | 250.8582 | 254.2983

## Slide 9: Capture Price Trend From a capture price perspective, which technology offers better potential between solar PV in GB and onshore wind in DE?
2022 Q3
Capture Trend ☀️ GB vs 💨 DE
Chart: 
| "22 | "23 | "24 | "25 | "26 | "27 | "28 | "29 | "30 | "31 | "32 | "33 | "34 | "35 | "36 | "37 | "38 | "39 | "40 | "41 | "42 | "43 | "44 | "45 | "46 | "47 | "48 | "49 | "50
GB-Solar PV | 178.092 | 155.574 | 119.274 | 93.798 | 77.586 | 72.954 | 68.322 | 63.69 | 60.216 | 61.374 | 59.058 | 59.058 | 57.9 | 55.584 | 55.584 | 55.584 | 53.268 | 53.268 | 50.952 | 49.794 | 47.478 | 46.32 | 45.162 | 45.162 | 45.162 | 45.162 | 45.162 | 46.32 | 45.162
DE-Onshore Wind | 211.0861 | 242.4324 | 170.8764 | 127.9632 | 105.6468 | 96.7716 | 81.3257 | 65.3749 | 54.7788 | 53.1254 | 50.8425 | 49.417 | 48.7103 | 47.9807 | 46.944 | 47.83 | 47.3014 | 48.1606 | 46.0492 | 45.1274 | 45.2911 | 44.6885 | 43.5777 | 41.9372 | 42.3692 | 41.391 | 40.2181 | 40.1597 | 38.8116
🏆
Long-Term Winner
☀️ Solar PV (GB)
Overtakes onshore wind post-2029 and maintains higher capture prices through 2050
Long Term-Median Capture Price
€50 €53
Solar PV Onshore Wind
Wind is +3% higher Overall
💡 Strategic Insight
While onshore wind (DE) shows higher capture prices initially and maintains a 3% median advantage, solar PV (GB) becomes more valuable from 2029 onwards, making it the superior long-term investment from a capture price perspective

## Slide 10: Capture Price Trend From a capture price perspective, which technology offers better potential between solar PV in GB and onshore wind in DE?
2023 Q1
Capture Trend ☀️ GB vs 💨 DE
🏆
CONSISTENT LEADER
☀️ Solar PV (GB)
Overtakes onshore wind post-2029 and maintains higher capture prices through 2050
Long Term-Median Capture Price
€62 €58
Solar PV Onshore Wind
Solar is +6.9% higher
💡 Strategic Insight
Onshore wind (DE) leads with 3% higher median initially, but Solar PV (GB) overtakes after 2029 and remains more valuable long-term, making it the better investment for future returns.
Chart: 
| "23 | "24 | "25 | "26 | "27 | "28 | "29 | "30 | "31 | "32 | "33 | "34 | "35 | "36 | "37 | "38 | "39 | "40 | "41 | "42 | "43 | "44 | "45 | "46 | "47 | "48 | "49 | "50
GB-Solar PV | 248.454 | 179.49 | 130.854 | 85.692 | 79.902 | 76.428 | 71.796 | 68.322 | 68.322 | 66.006 | 66.006 | 64.848 | 61.374 | 60.216 | 57.9 | 55.584 | 54.426 | 53.268 | 50.952 | 48.636 | 47.478 | 47.478 | 47.478 | 46.32 | 46.32 | 45.162 | 45.162 | 46.32
DE-Onshore Wind | 106.445 | 105.4181 | 95.7775 | 81.474 | 75.55 | 72.0322 | 67.7101 | 62.4575 | 61.444 | 59.8812 | 60.7845 | 59.1765 | 59.3637 | 59.3471 | 60.5065 | 60.7343 | 60.5962 | 58.2924 | 57.4378 | 56.9282 | 54.0727 | 52.7216 | 51.6262 | 49.4862 | 48.8729 | 47.647 | 46.7065 | 45.2279

## Slide 11
2022 Q3
Capture Price vs Generation
☀️Solar PV GB
CORRELATION ANALYSIS In the long run, is there a relationship between capture prices and power generation output (GWh) for solar PV and onshore wind in DE?
✅ Yes – Strong negative relationships. Solar PV shows very strong correlation (R = -0.89), Onshore Wind shows strong correlation (R = -0.70). As generation ↑, capture prices ↓
2022 Q3
Capture Price vs Generation
💨Onshore Wind DE
Chart: Generation (TWh)
| 12.4 | 13.68 | 14.69 | 17.100000000000001 | 19.41 | 21.83 | 23.27 | 24.73 | 25.95 | 25.95 | 27.05 | 28.16 | 29.35 | 30.56 | 32.32 | 33.92 | 35.51 | 37.15 | 38.799999999999997 | 40.65 | 42.5 | 44.89 | 46.86 | 48.18 | 50.8 | 51.79 | 53.52 | 54.56 | 55.68
Capture_Price Solar PV | 248.454 | 179.49 | 130.854 | 85.692 | 79.902 | 76.428 | 71.796 | 68.322 | 68.322 | 67.164 | 66.006 | 66.006 | 64.848 | 61.374 | 60.216 | 57.9 | 55.584 | 54.426 | 53.268 | 50.952 | 48.636 | 47.478 | 47.478 | 47.478 | 46.32 | 46.32 | 45.162 | 45.162 | 46.32
Chart: Generation (TWh)
| 97.361177923468404 | 102.53560080039701 | 108.094805843315 | 114.135544398044 | 120.33804308142599 | 124.19478506334499 | 129.42150510483799 | 134.711462570859 | 142.463170864098 | 147.77971279338399 | 154.22428552231901 | 158.36259266022799 | 163.56987627813001 | 169.66090109554301 | 171.36957830107801 | 175.23040123264599 | 179.87771719273999 | 185.18548941712299 | 192.19576368920701 | 200.06326738347701 | 209.01893592445199 | 218.019554994814 | 227.02345736335201 | 233.83521261996299 | 241.38459877090901 | 248.354717225602 | 257.49955126013202 | 264.51594595272798 | 270.96361320452502
Capture_Price Onshore Wind | 211.0861 | 242.4324 | 170.8764 | 127.9632 | 105.6468 | 96.7716 | 81.3257 | 65.3749 | 54.7788 | 53.1254 | 50.8425 | 49.417 | 48.7103 | 47.9807 | 46.944 | 47.83 | 47.3014 | 48.1606 | 46.0492 | 45.1274 | 45.2911 | 44.6885 | 43.5777 | 41.9372 | 42.3692 | 41.391 | 40.2181 | 40.1597 | 38.8116
Correlation
-0.89
R² = 0.7
⭐⭐⭐⭐⭐
Very Strong
79% of price variation explained by generation. Near-perfect inverse relationship.
Correlation
-0.70
R² = 0.49
⭐⭐⭐⭐
Strong
49% of price variation explained by generation. Clear inverse relationship
💡 Strategic Insight
Strong negative correlations indicate market saturation effects: as renewable capacity grows, capture prices decline due to merit order displacement and cannibalization. Solar PV's stronger correlation (R² = 0.79) suggests more predictable price dynamics

## Slide 12
2023 Q1
Capture Price vs Generation
☀️Solar PV GB
CORRELATION ANALYSIS In the long run, is there a relationship between capture prices and power generation output (GWh) for solar PV and onshore wind in DE?
✅ Yes – Strong negative relationships, strengthening over time. Solar PV maintains very strong correlation (R = -0.89), Onshore Wind correlation strengthened to R = -0.82 (from -0.70 in Q3). As generation ↑, capture prices ↓
2023 Q1
Capture Price vs Generation
💨Onshore Wind DE
Correlation
-0.89
R² = 0.7
⭐⭐⭐⭐⭐
Very Strong
79% of price variation explained by generation. Relationship remains unchanged from 2022Q3
Correlation
-0.82
R² = 0.67
⭐⭐⭐⭐ ⭐
Very Strong
67% of price variation explained by generation. Strengthened from Q3. Improved ↑ from -0.70
💡 Strategic Insight
Correlation strengthened for Onshore Wind (R: -0.70 → -0.82), indicating increasing market saturation concerns as renewable capacity grows. Both technologies now show very strong inverse relationships, suggesting more predictable cannibalization effects in the 2023 Q1 forecast scenario
Chart: Generation (TWh)
| 12.4 | 13.68 | 14.69 | 17.100000000000001 | 19.41 | 21.83 | 23.27 | 24.73 | 25.95 | 25.95 | 27.05 | 28.16 | 29.35 | 30.56 | 32.32 | 33.92 | 35.51 | 37.15 | 38.799999999999997 | 40.65 | 42.5 | 44.89 | 46.86 | 48.18 | 50.8 | 51.79 | 53.52 | 54.56 | 55.68
Capture_Price Solar PV | 248.454 | 179.49 | 130.854 | 85.692 | 79.902 | 76.428 | 71.796 | 68.322 | 68.322 | 67.164 | 66.006 | 66.006 | 64.848 | 61.374 | 60.216 | 57.9 | 55.584 | 54.426 | 53.268 | 50.952 | 48.636 | 47.478 | 47.478 | 47.478 | 46.32 | 46.32 | 45.162 | 45.162 | 46.32
Chart: Generation (TWh)
| 104.711351127806 | 107.41787820215799 | 114.166242238355 | 124.46941377187601 | 131.16961615934301 | 138.86348106324601 | 145.51520895469099 | 153.82905043837101 | 165.43161754103301 | 178.544896787167 | 188.33961517956899 | 199.571276480222 | 211.958577169867 | 224.63593696793799 | 235.771068242756 | 248.49131448771601 | 261.45305552047199 | 276.83365103867698 | 287.98570424926902 | 300.71809032100299 | 313.96852637619497 | 326.83620769824603 | 334.154420016887 | 343.482731392407 | 352.33031860510499 | 363.70666167300402 | 372.56379735633101 | 381.85357083943899
Capture_Price Onshore Wind | 106.445 | 105.4181 | 95.7775 | 81.474 | 75.55 | 72.0322 | 67.7101 | 62.4575 | 61.444 | 59.8812 | 60.7845 | 59.1765 | 59.3637 | 59.3471 | 60.5065 | 60.7343 | 60.5962 | 58.2924 | 57.4378 | 56.9282 | 54.0727 | 52.7216 | 51.6262 | 49.4862 | 48.8729 | 47.647 | 46.7065 | 45.2279

## Slide 13: Forecast Change Analysis (2022 Q3 → 2023 Q1) Did Aaron change his forecast for solar PV and onshore wind capture prices between Q3 2022 and Q1 2023? If so, how significant is the shift and what could possibly explain that?
⚠️ Yes – Significant upward revision. Solar PV capture price increased by 24% and Onshore Wind by 8%, reflecting evolving market conditions and lesson from 2022 energy crisis.
☀️ Solar PV (GB) +24% Median capture price increased from €50 to €62
Significant Shift
💨 Onshore Wind (DE) +8% Median capture price increased from €53 to €57
Moderate Shift
🔍Possible Explanations for Forecast Revisions
Energy Crisis Impact: Late 2022 European energy crisis led to reassessment of long-term wholesale price expectations, increasing projected capture prices.
Market Dynamics: Updated assumptions about baseload prices, grid flexibility, and storage deployment resulted in higher value projections for renewables
Industrial Demand: Revised industrial demand forecasts, particularly for electrification and hydrogen production, supporting higher electricity prices.
Policy Changes: EU policy responses to energy security (REPowerEU) and accelerated renewable targets influenced market price expectations.
Cost Inflation: Rising capital and operational costs for renewable projects translated into higher required revenue expectations in forecasts.

## Slide 14: Forecast Change Analysis (2022 Q3 → 2023 Q1) Did Aaron change his forecast for solar PV and onshore wind capture prices between Q3 2022 and Q1 2023? If so, how significant is the shift and what could possibly explain that?
⚠️ Yes – Significant upward revision. Solar PV capture price increased by 24% and Onshore Wind by 8%, reflecting evolving market conditions and lesson from 2022 energy crisis.
💡 Strategic Insight
The 24% and 8% upward revisions suggest Aaron incorporated lessons from the 2022 energy crisis and updated assumptions about long-term market structure. Higher capture prices in Q1 2023 forecast indicate more optimistic renewable value expectations, potentially driven by improved understanding of grid integration and policy support.

## Slide 15: SUMMARY OF KEY INSIGHT REPORT
2. Capture Price Trend
In both forecasts (2022Q3 and 2023Q1), Solar PV (GB) overtakes Onshore Wind (DE) after 2029, maintaining higher capture prices through 2050 Britain’s Solar PV demonstrates higher growth potential but greater short-term volatility.
Median capture price advantage: +6.9% for Solar PV in 2023Q1 forecasts.
4. Forecast Changes (2022Q3 → 2023Q1)
Solar PV capture prices revised upward by 24%, Onshore Wind by 8%.
Driven by the 2022 energy crisis, REPowerEU policy support, and rising cost structures in renewable projects.
1. Market Dynamics
Germany’s Onshore Wind shows strong long-term price stability.
Britain’s Solar PV demonstrates higher growth potential but greater short-term volatility.
By 2050, both countries’ baseload prices converge, indicating mature and balanced markets despite differing starting conditions.
3. Correlation and Market Saturation
Strong inverse correlations between generation and capture prices: Solar PV (R1 = -0.89, R2 = 0.79) Onshore Wind (R1 = -0.82, R2 = 0.67)
Indicates renewable cannibalization—as output increases, prices decline.

## Slide 16: CALL-TO-ACTION
Diversify Renewable Portfolios
Combine Germany’s stable Onshore Wind with Britain’s high-growth Solar PV to balance risk and return
Monitor Market Saturation
Strengthening negative correlation highlight the need for storage solutions and demand flexibility to offset cannibalization
Prioritize long term Solar PV investment in Britain
Despite Volatility, Solar PV offers superior long-run returns and resilience post 2029. Investors should position early to capture long term value growth.